## Slide 1: MAZE SOLVER
Marwan Jalaleddine
Yasmine Wehbe
Mosbah Aouad

## Slide 2: What Have we done?
We initialized the screen
We created the Main Menu
We created the modes
We created the algorithm

## Slide 3: Main Menu

## Slide 4: At first we initialize the registers
MOVLW d'5'
MOVWF OBSTACLES ;INITIALIZED MAX NUMBER OF OBSTACLES
MOVLW d'20'
MOVWF Count_Print_FSR
MOVLW d'1'
MOVWF S_Counter
MOVWF E_Counter
MOVLW d'0'
MOVWF I_1
MOVLW d'1'
MOVwf I_2

## Slide 5: We then write the Menu Options and go into an infinite loop
Call Default_Line ;We are going to the Default line
Call Menu_Flag ;We are setting the General Flag as Menu Flag
Call S_Pointer ;Setting a Pointer
Call L_D .
Call L_E .
Call L_F .
Call L_A
Call L_U
Call L_L
Call L_T
Notes: Here we should explain more

## Slide 6: INFINITE LOOP TATATADUM!
We put an infinite loop to accept interrupts!
BTFSC INTCON ,RBIF
GOTO RBIFINT
BTFSC INTCON, T0IF
GOTO TMR0INT
RBIFINT CALL DELAY1m
BTFSS PORTB,4
GOTO MOVE
BTFSS PORTB,5
GOTO CONFIRM
BTFSS PORTB,6
GOTO START_OL
BTFSS PORTB,7
GOTO END_OL
To select which interrupt we wish to service
If we have an interrupt on Port B we need to know which one changed

## Slide 7: Flags

## Slide 8: Flag General
No Bit is Set | We’re in the Menu
Bit 1 is Set | We’re in the Default Mode
Bit 2 is Set | We’re in the Obstacle Mode
Bit 3 is Set | We’re in the Maze Mode

## Slide 9: Interrupts
Depending on the interrupts we are going to Move or Confirm

## Slide 10: Move
BTFSC FlagGEN,0
CALL Move_Menu
BTFSC FlagGEN,2
Call Move_Mode_2
GOTO FOUNDIT
We only enable the move in the Menu and Mode
This choice depends on the Flag General

## Slide 11: Move Branching
Move_Menu BTFSC FlagMenu,0
GOTO Default_Menu
BTFSC FlagMenu,1
GOTO Obstacle_Menu
BTFSC FlagMenu,2
GOTO Maze_Menu
RETURN

## Slide 12: Confirms
Similarly , we service the confirms

## Slide 13
Confirm
Confirm Menu
Confirm Mode 2
Confirm Mode1
Confirm Mode 3
We choose either Mode 1 Mode 2 or mode 3
We Start the algorithm after pressing confirm
We put an obstacle here
We put an obstacle here
Notes: In each confirm we check the General flag and In modes 2 and 3 we check the number of remaining obstacles

## Slide 14: TIMER ZERO INTERRUPT
TMR0INT DECFSZ TMR0_COUNT, F
GOTO RET
CALL Move_Mode_3
MOVLW 0x20
MOVWF TMR0_COUNT
CLRF TMR0
RET BCF INTCON, 2
RETFIE

## Slide 15: Conventions

## Slide 16: INDF Conventions
Dash | 00000001
Block | 10000010
Start | 10000100
End | 10001000
Visited | 01000000

## Slide 17: WE CHOSE A CHALLENGING FSR
WE’RE NOT NORMAL YOU KNOW ;)

## Slide 18
FIRST ROW | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39
SECOND ROWN | 49 | 48 | 47 | 46 | 45 | 44 | 43 | 42 | 41 | 40
FSR SCREEN MAPPING
This challenging choice made it a more complex algorithm!

## Slide 19: How did we map the FSR to the LCD screen??

## Slide 20: The Star Function
CURSOR_right_position MOVF FSR,0
MOVWF COUNT4
MOVLW d'40'
SUBWF COUNT4,1
BTFSC STATUS,0
GOTO SECOND_LINE
GOTO FIRST_LINE

## Slide 21: If we’re on the first line, we adjust cursor to FSR address
FIRST_LINE MOVLW b'000000001'
MOVWF LINE_NUMBER
MOVF FSR,W
MOVWF COUNT4
MOVLW d'30'
SUBWF COUNT4,1
MOVLW B'01000';
Call LETTERS
MOVF COUNT4,W
Call LETTERS
return

## Slide 22: Similarly, for the second line we do the same!
SECOND_LINE MOVLW b'000000010'
MOVWF LINE_NUMBER
MOVLW d'49'
MOVWF COUNT4
MOVF FSR,W
SUBWF COUNT4,F
MOVLW B'01100';
Call LETTERS
MOVF COUNT4,W
Call LETTERS
Return

## Slide 23: How to Remove The Pointer??
RESET_MEMORY MOVLW d'20'
MOVWF COUNT8
MOVLW d'30'
MOVWF FSR

## Slide 24: This is just a loop inside Reset_Memory
TEMP_MEMORY BTFSC INDF,6
call REMOVE_POINTER
INCF FSR,F
DECFSZ COUNT8,F
GOTO TEMP_MEMORY
return

## Slide 25: Here, we effectively remove the Pointers
REMOVE_POINTER MOVLW b'00000001'
MOVWF INDF
call CURSOR_right_position
call S_DASH
return

## Slide 26: How did we go down?
DOWN_FSR MOVF FSR,w
MOVWF COUNT4 ; we did not call current position we just changed fsr
MOVLW d'30'
SUBWF COUNT4,F
MOVLW d'49'
MOVWF COUNT5
MOVF COUNT4,W
SUBWF COUNT5,W
MOVWF FSR
return

## Slide 27: How did we go up?
UP_FSR MOVLW d'49' MOVWF COUNT4
MOVF FSR,W
SUBWF COUNT4,F
MOVF COUNT4,W
ADDLW d'30'
MOVWF FSR
return

## Slide 28: Inserting a Block
Oh well 

## Slide 29
Inserting a Block:

## Slide 30: How did we Insert the Dashes?

## Slide 31
Print Dashes Function
PRINT_DASHES_TEMP CALL CURSOR_right_position
MOVLW b'00000001'
MOVWF INDF
CALL S_DASH
MOVLW d'49'
MOVWF COUNT4
MOVF FSR,W
SUBWF COUNT4,F
BTFSC STATUS,2
Return
INCF FSR,F
GOTO PRINT_DASHES_TEMP
return

## Slide 33: The Algorithm!
Let’s be serious!

## Slide 34: Problems we faced while designing it
To go right on first line , we increment
To go right on second line we decrement
To go left on first line , we decrement
To go left on second line we increment
To go up, we needed to use a formula (not so straight forward)
To go down, we also needed to use a formula (which required difficult to ) design functions

## Slide 35: Let’s Get Started!

## Slide 36: Right
Go_Right CALL CURSOR_right_position
BTFSS LINE_NUMBER,1
GOTO Go_Right_first_line if we’re on the 1st line
GOTO Go_Right_second_line if we’re on the 2nd line
If we’re up we don’t do next Instruction

## Slide 37: When We’re on the first line, we increment

## Slide 38: If we’re on the second line we decrement

## Slide 39: Similarly we do the Go_Left
But with different FSR values (and we go to Up afterwards)

## Slide 40: Go Up!

## Slide 41: GO GO GO DOWN!